## Slide 1: SECON 2015
Midterm Presentation

## Slide 2: The Team
Bryce Amacker
Team Leader
Steven Calhoun
Dexter Duckworth
Ben Eisman
Ryant Nelson
Faith Smith
Tran Ton
Dr. J.W. Bruce
Faculty Advisor

## Slide 3: Outline
Competition Overview
Practical Constraints
  Sustainability
  Environmental
Technical Constraints
  Autonomous Navigation
  Speed
  LED Start
  Toy Tasks
    Simon
    Rubik’s Cube
    Playing Card
    Etch-a-Sketch
Other Technical Considerations
Timeline
References

## Slide 4: Competition Overview
Start upon red LED shutoff
Sample Course
Finish

## Slide 5: Points System
Task | Points
Robot starting upon red LED shutoff | 100 points, disqualified if unable to start
Navigating to each station | 10 points per station. There are four stations. 40 total points possible.
Playing Simon without error | 10 points per second, up to 15 seconds. 150 total points possible.
Drawing “IEEE” | 50 points per letter. 200 total points possible.
Rotate top panel of Rubik’s cube 180 degrees. | 50 points
Pick up card and carry across the finish line | 50 points
Speed, efficiency, engineering excellence. | Undetermined amount of points
Finishing before the 5 minutes is up. | 300 - the time in seconds it took to cross the finish line.

## Slide 6: Sustainability
Problem | Solution
The course must be completed in 5 minutes or less. There is an uncertain amount of time between rounds of competition. | We will select a rechargeable battery with a life of at least 20 minutes. We will use fresh batteries in competition to ensure optimal conditions.

## Slide 7: Environmental
Problem | Solution
Competition space will be full of spectators, competitors, and judges making noise. The team will be unable to control the light levels in the competition space. | Any light or sound sensors used (especially those need for starting upon the red light and solving the Simon) must operate within a certain tolerance for unknown conditions. This has been a problem for past teams.

## Slide 8: Technical Constraints
Name | Description
Navigation | The robot must navigate the course autonomously and locate the white squares that indicate the location of the toys.
Speed | The robot must navigate through the course and play with each toy in less than 5 minutes.
Size | The robot must fit within a 1' x 1' x 1' space at the start and finish of the course.
LED Start | The robot must being course navigation upon the shutoff of a red LED.
Toy Tasks | The robot must be able to perform various tasks with certain pre-selected toys.

## Slide 9: LED Start
Requirements
The robot must start course upon detection of LED off
Approach
Use photoresistor as sensor to detect light
Shield ambient light from resistor
Considerations
Photoresistor sensitivity unpredictable
Ambient light shield could encourage “false start”
Course LED could be flush with plane or raised/lowered

## Slide 10: LED Start: Prototype

## Slide 11: Autonomous Navigation
Requirements
Autonomously navigate a flat course using white lines on the floor
Recognize and approach squares containing toys
Approach
Two-level navigation system
High-level autonomy using the Robot Operating System (ROS) on a Beaglebone
Low-level motor control using a PID controller on an Arduino
Considerations
Speed
Localization
Accuracy

## Slide 12: Motor Controller
Powered by an Arduino
Uses motor encoders to determine wheel position and velocity
Converts wheel positions into robot odometry data
Uses a PID controller model to match and maintain a target velocity
Uses a serial interface to send odometry and receive commands
[2]
[3]

## Slide 13: Autonomy
Implemented using ROS Hydro
Will use a line follower sensor to build a costmap of the course
Will identify intersections and other landmarks in order to find toys
Robust to unknown course layouts
Efficient at navigating known course layouts
Communicates with the motor controller using the rosserial package
[4]
[5]

## Slide 14: Toy Tasks
Play Simon Says for 15 seconds
Rotate Rubik's Cube 180°
Pick Up a single playing card from a full deck
Draw “IEEE” on an Etch-a-Sketch

## Slide 15: Simon
Requirements
Ability to depress all 5 buttons on toy
Must detect the correct buttons to press
Approach
Attach photoresistors to each of the arms used to press buttons
Monitor photoresistors’ data and record buttons that light up
Play back this sequence by pressing the buttons with servo controlled arms
Considerations
Ambient light can affect photoresistor processing
Different Simon toys may produce different amounts of light

## Slide 16: Simon Prototype

## Slide 17: Simon Demo

## Slide 18: Rubik’s Cube
Requirements
Spin just the top layer of the cube 180°
Approach
Swing instrument down on top of cube
Rotate instrument, spinning the cube
Considerations
Newer cubes require more force to rotate compared to frequently used cubes

## Slide 19: Rubik’s Cube Prototype

## Slide 20: Rubik’s Cube Demo

## Slide 21: Playing Card
Requirements
Retrieve a single card from a deck of cards
Approach
Navigate to deck of cards
Press down on top of deck with sticky material and lift up
Considerations
Misalignment between instrument and deck
Sticky material not successfully grabbing card

## Slide 22: Etch-a-Sketch
Requirements
Draw the letters “IEEE” on an Etch-a-Sketch
Approach
Pull Etch-a-Sketch into robot with an arm
Move two servers with cone shaped grippers over the knobs of the Etch-a-Sketch
Spin each knob for precise amounts of time
Considerations
Varying levels of grip on each arm
Inconsistency in Etch-a-Sketch drawing mechanisms
Speed differences between continuous servos
IEEE

## Slide 23: Etch-a-Sketch Prototype

## Slide 24: Etch-a-Sketch Demo

## Slide 25: Other Technical Considerations
Integration
  Unified mechanical device that will manipulate toys incorporating
  Make sure each toy’s prototype do not interfere each other
Weight
  Heavy robot requires larger motors and higher-capacity batteries
  Manage Weight distribution over the base of the robot

## Slide 26: Processors
Options | Pros | Cons
PIC24H | More I/O ports Inexpensive Experience from class work Resources from ECE faculty Code from previous SECON teams | Platform not included More complex to program and debug
Arduino | Platform included Easy-to use hardware & software Great online community support | Not enough I/O ports Expensive

## Slide 27: Timeline
 | Aug | Sep | Oct | Nov | Dec
Course Construction & Strategy |  |  |  |  | 
Research & Purchasing |  |  |  |  | 
Programming |  |  |  |  | 
Circuit Design |  |  |  |  | 
Debugging |  |  |  |  | 
Prototype |  |  |  |  | 

## Slide 28: References
[1] Institute of Electrical and Electronic Engineers Southeastern Conference (IEEE SECON) Rules Internet: https://www.facebook.com/notes/2015-ieee-southeastcon/hardware-competition-overview-and-rules/657025027666068 (Accessed: 2 September , 2014)
[2] PID controller, Wikipedia, [online] 2014, http://en.wikipedia.org/wiki/PID_controller (Accessed: 29 September 2014)
[3] Arduino Diecimila, Arduino, [online], http://arduino.cc/en/Main/ArduinoBoardDiecimila (Accessed: 29 September 2014)
[4] T. Foote, “ROS Hydro Medusa Released!,” (ROS.org), [online] 9 September 2013, http://www.ros.org/news/2013/09/ros-hydro-medusa-released.html (Accessed: 29 September 2014)
[5] costmap_2d, ROS.org, [online] 2008, http://wiki.ros.org/costmap_2d (Accessed: 29 September 2014)

## Slide 29: SECON 2015
Midterm Presentation